So I want to
1. run myIMU.MPU9250SelfTest(myIMU.SelfTest)
    myIMU.SelfTest is an array containing the percentage of factor value the trim is within as a float.
2. Run myIMU.calibrateMPU9250(myIMU.gyroBias, myIMU.accelBias);
    myIMU.gyroBias and myIMU.accelBias are float arrays containing the Bias values to be subtracted. Oddly, the example code doesn't ever use the gyro bias, just the accel bias.
3. Run the getXres() functions
    xRes variables contain mode specific multipliers that convert from raw data to gravities or degrees per second or gauss
4. Run myIMU.initMPU9250
    Sets up the IMU for active data read

5. Add the gyro angular velocities to a rolling sum to estimate the current position.
  float pitch_gyro_delta = imu_data[0]*imu_diff;
  float roll_gyro_delta = imu_data[1]*imu_diff;
  //Similar for Yaw

6. Estimate roll and pitch with the accelerometer. use atan2(y/z) for roll, atan2(x/z) for pitch.
  float pitch_accel = (atan2(imu_data[4],imu_data[5]))*180.0/3.1415 - pitch_calibration;
  float roll_accel = (atan2(imu_data[3],imu_data[5]))*180.0/3.1415 - roll_calibration;

7. Add the estimates with a complementary filter
  roll_angle = roll_accel*A + (1-A)*(roll_gyro_delta + roll_angle);
  pitch_angle = pitch_accel*A + (1-A)*(pitch_gyro_delta + pitch_angle);

8. Send the estimated roll, pitch, and yaw over serial to be picked up by the listener node, then publish
  Serial.print(myIMU.mx); Serial.print(","); Serial.print(myIMU.my); Serial.print(","); Serial.print(myIMU.mz);
  Serial.print(","); Serial.print(Roll); Serial.print(","); Serial.print(Pitch); Serial.print(","); Serial.print(Yaw); Serial.print("\n");
9. Subscribe with a processor node and publish a tf or frame message of some sort to get the data displayed in rviz.